## Slide 1: CSE101 Intro to CS and Programming
Lecture 11 (Week 6)
By Mr. Faheem Shaukat
faheem@iqraisb.edu.pk
www.tinyurl.com/IUICLectures
Boolean Algebra and Logic Circuits

## Slide 2
CCoommppuutterer FFununddaammenenttaallss:: PPrradadeeeepp KK.. SSiinhnhaa && PPrriititi SSiinhanha
Ref Page Chapter 5: Computer Arithmetic Slide 1/29

## Slide 3: Learning Objectives
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
In this chapter you will learn about:
Reasons for using binary instead of decimal numbers
Basic arithmetic operations using binary numbers
  Addition (+)
  Subtraction (-)
  Multiplication (*) (Out of Course)
  Division (/) (Out of Course)
Slide 3/29
49

## Slide 4: Binary over Decimal
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Information is handled in a computer by electronic/ electrical components
Slide 4/29
49
Electronic components
operate in binary mode (can
only indicate two states – on (1) or off (0)
Binary number system has only two digits (0 and 1), and is suitable for expressing two possible states
In binary system, computer circuits only have to handle two binary digits rather than ten decimal digits causing:
Simpler internal circuit design
Less expensive
More reliable circuits
with
binary
Arithmetic rules/processes possible numbers

## Slide 5: Examples of a Few Devices that work in Binary Mode
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Binary State | On (1) | Off (0)
Bulb |  | 
Switch |  | 
Circuit Pulse |  | 
Slide 5/29
50

## Slide 6: Binary Arithmetic
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Binary arithmetic is simple to learn as binary number system has only two digits – 0 and 1
Following slides show rules and example for the four basic arithmetic operations using binary numbers
Slide 6/29
50

## Slide 7: Binary Addition
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Rule for binary addition is as follows:
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 0 plus a carry of 1 to next higher column
Slide 7/29
50

## Slide 8: Binary Addition (Example 1)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Add binary numbers 10011 and 1001 in both decimal and binary form
Solution
Slide 8/29
51
Decimal
11100 28
In this example, carry are generated for first and second columns
Binary
carry 11
10011
+1001
carry 1
19
+9

## Slide 9: Binary Addition (Example 2)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Add binary numbers 100111 and 11011 in both decimal and binary form
Solution
Binary
Decimal
1000010
carry | 11111 | carry | 1
 | 100111 |  | 39
 | +11011 |  | +27
The addition of three 1s
Slide 9/29
51
can be broken up into two
66
steps. First, we add only two 1s giving 10 (1 + 1 =
10). The third 1 is now added to this result to
obtain 11 (a 1 sum with a 1
carry). Hence, 1 + 1 + 1 = 1, plus a carry of 1 to next higher column.

## Slide 10: Binary Subtraction
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Rule for binary subtraction is as follows:
0 - 0 = 0
0 - 1 = 1 with a borrow from the next column 1 - 0 = 1
1 - 1 = 0
Slide 10/29
51

## Slide 11: Binary Subtraction (Example)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Subtract 011102 from 101012
Solution
12
0202
10101
-01110
00111
Note: Go through explanation given in the book
52

## Slide 12: Complement of a Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Complement of the number
Base of the number
C
=
Bn
-
1
- N
Number of digits in the number
The number
52

## Slide 13: Complement of a Number (Example 1)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Find the complement of 3710
Solution
Since the number has 2 digits and the value of base is 10,
(Base)n - 1 = 102 - 1 = 99
Now 99 - 37 = 62
Hence, complement of 3710 = 6210
53

## Slide 14: Complement of a Number (Example 2)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Find the complement of 68
53
number has 1 digit and the value of
Solution
Since the base is 8,
(Base)n - 1 = 81 - 1 = 710 = 78
Now 78 - 68 = 18
Hence, complement of 68 = 18

## Slide 15: Complement of a Binary Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Complement of a binary number can be obtained by transforming all its 0’s to 1’s and all its 1’s to 0’s
Example
Complement of
1 0 1 1 0 1 0 is
0 1 0 0 1 0 1
Note: Verify by conventional complement
53

## Slide 16: Complementary Method of Subtraction
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Involves following 3 steps:
53
the number you
from
which you
Step 1: Find the complement of are subtracting (subtrahend)
Step 2: Add this to the number are taking away (minuend)
Step 3: If there is a carry of 1,
add it to obtain
the result; if there is no carry, recomplement the sum and attach a negative sign
Complementary subtraction is an additive approach of subtraction

## Slide 17: Complementary Subtraction (Example 1)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example:
Subtract 5610 from 9210 using complementary method.
53
Solution
Step 1: Complement of 5610
= 102 - 1 - 56 = 99 – 56 = 4310
Step 2: 92 + 43 (complement of 56)
= 135 (note 1 as carry)
Step 3: 35 + 1 (add 1 carry to sum)
Result = 36
The result may be verified using the method of normal subtraction:
92 - 56 = 36

## Slide 18: Complementary Subtraction (Example 2)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Subtract 3510 from 1810 using complementary method.
Solution
53
Step 1: Complement of 3510
= 102 - 1 - 35
= 99 - 35
= 6410
Step 2:
18
+ 64 (complement
of 35)
82
Step 3: Since there is no carry,
re-complement the sum and attach a negative sign to
obtain the result.
Result
= -(99 - 82)
= -17
The result may be verified using normal subtraction:
18 - 35 = -17

## Slide 19: Binary Subtraction Using Complementary Method (Example 1)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Subtract 01110002 (5610) from 10111002 (9210) using complementary method.
Solution
1011100
+1000111 (complement of 0111000)
10100011
1 (add the carry of 1)
0100100
Result = 01001002 = 3610
53

## Slide 20: Binary Subtraction Using Complementary Method (Example 2)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Subtract 1000112 (3510) from 0100102 (1810) using complementary method.
Solution
010010
+011100 (complement of 100011)
101110
Since there is no carry, we have to complement the sum and attach a negative sign to it. Hence,
Result = -0100012 (complement of 1011102)
= -1710
54

## Slide 21
CCoommppuutterer FFununddaammenenttaallss:: PPrradadeeepep KK.. SSiinhanha && PPrriititi SSiinhanha
Ref. Page Chapter 6: Boolean Algebra and Logic Circuits Slide 1/78

## Slide 22: Learning Objectives
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
In this chapter you will learn about:
Fundamental concepts and basic laws of Boolean algebra
Boolean function and minimization
Logic gates
Logic circuits and Boolean expressions
60
Slide 22/78

## Slide 23: Fundamental Concepts of Boolean Algebra
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Use of Binary Digit
  Boolean equations can have either of two possible values, 0 and 1
Logical Addition
  Symbol ‘+’, also known as ‘OR’ operator, used for logical addition. Follows law of binary addition
Logical Multiplication
  Symbol ‘.’, also known as ‘AND’ operator, used for logical multiplication. Follows law of binary multiplication
Complementation
  Symbol ‘-’, also known as ‘NOT’ operator, used for complementation. Follows law of binary compliment
61
Slide 23/78

## Slide 24: Operator Precedence
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Higher the operator’s precedence level, earlier it is evaluated
Expression is scanned from left to right
First, expressions enclosed within parentheses are evaluated
Then, all complement (NOT) operations are performed
Then, all ‘’ (AND) operations are performed
Finally, all ‘’ (OR) operations are performed
62
Slide 24/78
(Continued on next slide)

## Slide 25
1st
62
Slide 25/78
2nd
3rd
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Operator Precedence
(Continued from previous slide..)
X  Y  Z

## Slide 26: Boolean Functions
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
A Boolean function is an expression formed with:
  Binary variables
  Operators (OR, AND, and NOT)
  Parentheses, and equal sign
The value of a Boolean function can be either 0 or 1
A Boolean function may be represented as:
  An algebraic expression,
  A truth table
  Logical Circuit
67

## Slide 27: Representation as an Algebraic Expression
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
W = X + Y ·Z
Variable W is a function of X, Y, and Z, can also be written as W = f (X, Y, Z)
The RHS of the equation is called an expression
The symbols X, Y, Z are the literals of the function
For a given Boolean function, there may be more than one algebraic expressions
67

## Slide 28: Representation as a Truth Table
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
X | Y | Z | W
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
67
(Continued on next slide)

## Slide 29: Representation as a Truth Table
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
The number of rows in the table is equal to 2n, where
n is the number of literals in the function
The combinations of 0s and 1s for rows of this table are obtained from the binary numbers by counting from 0 to 2n - 1
67
(Continued from previous slide..)

## Slide 30: Logic Gates
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Logic gates are electronic circuits that operate on one or more input signals to produce standard output signal
Are the building blocks of all the circuits in a computer
Some of the most basic and useful logic gates are AND, OR, NOT, NAND and NOR gates
77

## Slide 31: AND Gate
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
realization
77
of logical
multiplication
(AND)
Physical operation
of 1 only if all input
Generates an output signal signals are also 1

## Slide 32: AND Gate (Block Diagram Symbol and Truth Table)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
A B
C = A  B
Inputs |  | Output
A | B | C = A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
77

## Slide 33: OR Gate
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Physical realization of logical addition (OR) operation
Generates an output signal of 1 if at least one of the input signals is also 1
77

## Slide 34: OR Gate (Block Diagram Symbol and Truth Table)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
C = A + B
A
B
Inputs |  | Output
A | B | C = A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
78

## Slide 35: NOT Gate
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Physical realization of complementation operation
Generates an output signal, which is the reverse of the input signal
78

## Slide 36: NOT Gate (Block Diagram Symbol and Truth Table)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
A
A
Input | Output
A | A
0 | 1
1 | 0
79

## Slide 37: NAND Gate
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Complemented AND gate
Generates an output signal of:
  1 if any one of the inputs is a 0
  0 when all the inputs are 1
79

## Slide 38: NAND Gate (Block Diagram Symbol and Truth Table)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
A
B
C= A B= A B= A +B
Inputs |  | Output
A | B | C = A +B
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
79

## Slide 39: NOR Gate
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Complemented OR gate
Generates an output signal of:
  1 only when all inputs are 0
  0 if any one of inputs is a 1
79

## Slide 40: NOR Gate (Block Diagram Symbol and Truth Table)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
A
B
C= A B= A B= A  B
Inputs |  | Output
A | B | C = A  B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
80

## Slide 41: Logic Circuits
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
When logic gates are interconnected to form a gating / logic network, it is known as a combinational logic circuit
The Boolean algebra expression for a given logic circuit can be derived by systematically progressing from input to output on the gates
The three logic gates (AND, OR, and NOT) are logically complete because any Boolean expression can be realized as a logic circuit using only these three gates
80

## Slide 42: Finding Boolean Expression of a Logic Circuit (Example 1)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
B C
A
A
NOT
OR
B + C
D= A B + C
80
AND

## Slide 43: Finding Boolean Expression of a Logic Circuit (Example 2)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
A B
NOT
OR
C=A +BA B
A B
AND
A  B
AB
81
AND

## Slide 44: Constructing a Logic Circuit from a Boolean Expression (Example 1)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
OR
A B
AND
A B +C
83
A B
C
Boolean Expression =
A B +C